## Slide 1
Scaling tomo + prop to whole-brain volumes
Key idea: every 2-D operator is separable → we only run 1-D computations
Tomo — USFFT Radon
obj
·φ
FFT_x
FFT_y
gather
IFFT_r
sino
φ(x, y) = φ₁ᴅ(x) · φ₁ᴅ(y) → stored as 2 vectors of length n
c2d(x, y) = c2d₁ᴅ(x) · c2d₁ᴅ(y) → 2 vectors of length 2n
(x₀, y₀) = (cos θₖ · r, −sin θₖ · r) → recomputed inside CUDA gather kernel
Prop — Fresnel angular-spectrum
ψ
FFT_x
·K_x(fx)
FFT_y
·K_y(fy)
IFFT_y
IFFT_x
K(fx, fy) = exp(−iπλL(fx² + fy²)) = K_x(fx) · K_y(fy)
Fresnel kernel is separable in the Fourier domain — stored as 2 vectors of length 2n.
Never allocated (would dominate at large N):
who
2-D object
naive size
what we store instead
Tomo
φ (n × n) c64
n² · 8 B
2 vectors × n c64 (~ MB)
Tomo
c2dfftshift (2n × 2n) i8
(2n)² · 1 B
2 vectors × 2n i8 (~ KB)
Tomo
x, y sample tables f32
2 · nθ · n · 4 B
recomputed in kernel from (cos θ, sin θ, idx)
Prop
K (2n × 2n) c64
(2n)² · 8 B
2 vectors × 2n c64 (~ MB)
Second-order tricks that ride the 1-D structure
Host-staged 2-D grid
the full 2N × 2N Fourier grid lives PINNED on host; GPU sees only per-pass strips
→ GPU peak fixed at ~35 GB regardless of N
Banded pinned memory
one 576 GB cudaHostAlloc → 4–8 blocks of ≤ 144 GB each
→ fits under NVIDIA driver’s per-alloc cap
Streamed 3-way pipe
load ‖ compute ‖ store per chunk with 2× ping-pong pinned buffers
→ overlap hides H2D / D2H latency